## Slide 1: CanCURVE
Heather McGrath
Nicky Hastings
Lisa Landon-Roy
March 2024

## Slide 2: Background
There are a lack of Canadian specific damage curves to assess risks from floods
Damage curves are a key methodological piece in the calculation of impacts and consequences from a natural hazard event
Flood risk assessments in Canada have historically relied on curves from FEMA, generic curves from the UK multi coloured manual or Australian National curves
From damages calculated to buildings, impacts to people (displacement, disruption, etc.), and economic impacts can be interpreted

## Slide 3: Overview
New method for development of stage-damage functions for buildings
  Transparent calculation methodology
  In-line with industry cost estimators
  Canadian made tool for Canadian buildings
  Support for geographic variability
Features:
  Open source tool
  Composite level information
  Support for non-traditional building archetypes
  Probabilistic modelling
  Ability to change spatially/temporally the damage function

## Slide 4: Metholology
  Tiered approach
    link line items to rooms, rooms to room definitions, and room definitions to buildings via a Master Rule Book
  Benefits:
    Mix and match:
      Default room configurations
      User modifiable
    Can add items and pricelists
    Formal building archetypes are not required

## Slide 5: Multi-level results
Every line item essentially has it’s own depth-damage curve
‘roll-up’ to create damage curve for the whole structure
‘drill-down’ to view component curves e.g.:
  Level: 1st floor, basement, etc.
  Room: kitchen, bedroom, etc.

## Slide 6: Base structure:

## Slide 7: Transparency of origin
Contain metadata which describes details of their creation

## Slide 8: Prototype ---> Application
Currently an excel prototype exists
  Limited data for backend Master Rulebook
    Single family residential homes
    Structural losses only
    Requires Xactimate files
Contract just started
  To program it in Python
  More robust
  Integrate with CanFlood
  User friendly
  FEATURES:
    Users can Browse Library of existing curves (very limited- presently)
    Users can build/develop their own curves
    Users can upload their own backend data (line items, costing, to develop curves)
Draft expected May 2024

## Slide 9: Backend Data (Master Rulebook)
Looking to add more data (line items) and rooms/archetype definitinos

## Slide 10: Program Mockup
DDF
User enter:
General Building
Input
Room Specification
based on occupancy
Defaults + user edits

## Slide 11: Proposed structure
Backend databases
  MasterRuleBook
    Contains all unique items – construction and content related
      E.g.: drywall, flooring, baseboard, sink, etc.
      Primary KEY: Cat.Sel
    Contains : depth replacement value, 0 to 1 for each Cat.Sel
    Contains: cost, by location and date
Example: MasterRuleBook_LineItems.xls
MasterRuleBook
Line Items
All items found in a building: structural and contents
Depth Replacement
Unique list and value for each item at each water depth
$
(by location & date)
Unique list and value for each item at each place & time
Cat.Sel = unique identifier
Columns :Fixed : based on water depths
Rows: Variable
Columns : variable based on location and price list data
Rows: variable

## Slide 12: Proposed Databases
User Input fields: (UIGeneralInfo.xlsx)
  To populate GUI
Masterlist (MasterRuleBook_LineItems.xlsx)
  All LineItems, costing, depth replacement
Room Specifications (ItemsByArchType.csv)
  LineItems per room type, quantity, group(s) and building archetype
Room Dimensions (RoomDimensions.csv)
  Based on Building Archetype

## Slide 13: GUI Mockup
Preliminary suggestions – open to discussion

## Slide 14: GUI Mockups:
Browse Existing Library
Create New Curve
Welcome to CanCurve

## Slide 15: Create New Section:
Welcome to CanCurve
Browse Existing Library
Create New Curve

## Slide 16: Mockup: Page 1 General Input
Curve Name | 
What location are you interested in? | 
What timeframe do you want the prices to reflect? | 
What type of DDF (Depth Damage Function) do you want to create? | 
What type of structure are you interested in? | 
If Residential: | 
How many storeys or levels are there? | 
What is the estimated square footage or square meters of the structure? | 
What are the quality of the finishes? | 
Does it have a basement? | None/Basement/Crawlspace
*Is the basement developed? | Finished Unfinished
**If Yes: Percent Developed (0 to 100) 100 == fully developed= default = 0 | 
What level is the mechanical equipment located on? | 
What type of Heating is there? | 
What type of Cooling (if any)? | 
What is the height of the first floor (m) from the ground elevation? | 
Maybe instead of a ist of questions, it's pages(s) with pictures a user selects with text below?
General Info
Room Details/Levels
Generate DDF
Create New Curve
Add Pricelist
Add Location
NEXT
Notes: All of the specifications/requirements to be captured as metadata and requirements for development of the DDF

## Slide 17: Mockup Page 3: Room Dimensions
Bedroom
Bathroom
From ItemsByArchType.csv – need to look at Group.Description & Group2 columns of buildarchtype column filtered by A_B-C-DE-FF
Hallway
Kitchen
Maybe a figure? Of the rooms and how they are hypothetically laid out and their sizes?
Walkincloset
Dining
Bedroom
Family
UtilityRoom
?
Add Room
General Info
Residential
Room Details/Levels
Generate DDF
Rooms | Total | Main Level | Basement | Upper Level
1.5 Bath | 1 | 1 | 0 | 0
Bedroom | 9 | 5 | 4 | 0
Dining Room | 1 | 1 | 0 | 0
Entry Foyer | 2 | 1 | 0 | 0
Full Bath | 3 | 1 | 2 | 0
Half Bath | 2 | 1 | 0 | 0
Hallway | 4 | 2 | 2 | 0
Kitchen | 1 | 1 | 0 | 0
Laundry Room | 3 | 1 | 1 | 0
Living Area | 4 | 2 | 2 | 0
Nook | 2 | 1 | 1 | 0
Utility Room | 2 | 1 | 1 | 0
Walk-In Closet | 2 | 1 | 1 | 0
Advanced Settings (Optional)
Read from items by “ItemsByArchType”
Generates dynamically - DEFAULT
…
Suggest: user can override -add room/change room
NEXT
BACK
Notes: Describe what needs to be done by the user.
User needs to specify the details for each room

## Slide 18: Mockup Page 3: Room Dimensions
Save
General Info
Residential
Room Details/Levels
Generate DDF
Advanced Settings (Optional)
Add Room
From RoomDimensions.csv
Takes you back to previous page (Residential
Room Details/Levels)

## Slide 19: Mockup Page 3: Room Dimensions
Create New Curve
Bedroom
Bathroom
Combination of: ItemsByArchType.csv – need to look at Group.Description & Group2 columns of buildarchtype column filtered by A_B-C-DE-FF & RoomDimensions.csv filtered/queried by: buildingType, buildingSize, buildignBasement buildingQuality
Default From UI RoomDetails, user can overwrite Levels from previous page
Hallway
Kitchen
Maybe a figure? Of the rooms and how they are hypothetically laid out and their sizes?
Walkincloset
Dining
Bedroom
Family
UtilityRoom
?
Room Dimensions
General Info
Room Details/Levels
Generate DDF
Advanced Settings
Room Contents
Depth Response
Save
Notes: Describe what the user needs to do...

## Slide 20: Mockup Page 3: Room Dimensions
Create New Curve
Bedroom
Bathroom
ItemsByArchType.csv
Hallway
Kitchen
Maybe a figure? Of the rooms and how they are hypothetically laid out and their sizes?
Walkincloset
Dining
Bedroom
Family
UtilityRoom
?
Room Dimensions
General Info
Room Details/Levels
Generate DDF
Advanced Settings
Room Contents
Depth Response
Save
Notes: Describe what the user needs to do...

## Slide 21: Mockup Page 3: Room Dimensions
Create New Curve
Bedroom
Bathroom
From: MasterRuleBook_LineItems: Depth Replacement worksheet
Hallway
Kitchen
Maybe a figure? Of the rooms and how they are hypothetically laid out and their sizes?
Walkincloset
Dining
Bedroom
Family
UtilityRoom
?
Room Dimensions
General Info
Room Details/Levels
Generate DDF
Advanced Settings
Room Contents
Depth Response
Save
Notes: Describe what the user needs to do...

## Slide 22: Mockup Page 4: Run the calculations
Summary of input: | 
Pricelist: | 
Type | 
Levels: | 
Quality: | 
… | 
… | 
… | 
… | 
DDF Curve XXX is generated
RUN
(Generate Curve)
Results
When complete, download file option: with DDF and report/log of all the input and some of the data/tables used.
General Info
Room Details/Levels
Generate DDF
Explore &
Visualize
Download
Notes: Define file types for the resulting DDF – report? Csv file?

## Slide 23: UI Mockups:
Welcome to CanCurve
Browse Existing Library
Create New Curve

## Slide 24: Browse Existing:
Browse By:
Library
Location
Building Type
Download (single or multiple)
Date
Functions for each of these tabs:
Select
View curve(s) graphically
View metadata
Download
Curve
Metadata
Browse Existing Library
From: \ExistingLibrary\ there are xls. That can be read in for this…maybe there is a better way to read/store/access

## Slide 25: Calculations
Refer to XLS samples

## Slide 26: DDF: Calculations: Get Data
ItemList
Costs : XXYY
Depths
Factor: XXYY

## Slide 27: Sum by Group 2
Group 2: Sum costs per water depth
  Not all – necessarily, but could have:
    Group2.Mech
    GroupBasem
    Split
    Main
    Upper
Depth | main | mechanical | split | upper | basement | Grand Total
 | GM | GMech | GS | GU | GB | 
-0.9 | $0 | $0 | $0 | $0 | $0 | $0
-0.46 | $0 | $0 | $0 | $0 | $0 | $0
0 | $0 | $0 | $0 | $0 | $0 | $0
0.03 | $14,866 | $0 | $3,523 | $17,207 | $13,806 | $49,401
0.05 | $26,497 | $0 | $5,678 | $27,524 | $20,917 | $80,615
0.1 | $28,347 | $1,577 | $5,678 | $27,524 | $20,917 | $84,042
0.15 | $31,733 | $5,624 | $5,781 | $27,569 | $20,917 | $91,624
0.3 | $31,733 | $5,624 | $5,962 | $27,569 | $20,917 | $91,805
0.46 | $35,760 | $5,624 | $18,020 | $31,147 | $23,997 | $114,548
0.61 | $36,339 | $5,624 | $18,124 | $35,505 | $25,575 | $121,167
0.76 | $38,763 | $5,624 | $19,148 | $39,535 | $27,590 | $130,660
0.91 | $49,217 | $7,645 | $21,882 | $53,792 | $37,096 | $169,632
1.02 | $53,342 | $7,645 | $29,027 | $54,405 | $37,096 | $181,516
1.22 | $53,646 | $7,645 | $29,582 | $54,597 | $37,149 | $182,619
1.52 | $55,784 | $7,645 | $29,814 | $56,838 | $38,808 | $188,889
1.83 | $55,784 | $15,148 | $29,814 | $56,838 | $38,808 | $196,391
2.7 | $55,784 | $15,148 | $29,814 | $56,838 | $38,808 | $196,391

## Slide 28: Master list water depths :
The Water depths, in the master list, relate to depth of water above the floor (any floor level)
e.g.:
  for a basement or a main floor, 0 is the floor, the surface you walk on.
  0.3 = height of bottom of electrical outlet – basement or main floor

## Slide 30: Variables needed for calculations:

## Slide 31: This is data from Slide 25 – once you ‘sum’ by Group2 category.

## Slide 32: Calc 1: Basement
Depth | Equation: | Example: (referencing previous slide data) | Values | Calculated: | WHAT IT SHOULD BE | Difference?
-2.7 | ( Gmech + GS/2 + GB ) * FV | (C5 + D5/2 + F5) * FV | (0 + 0/2 + 0) * 1 | $0 | $0 | $0
-2.67 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C6 + D6/2 + F6 + RC_B) * FV | (0 + 3523/2 + 13806 + 11553) * 1 | $27,121 | $27,120 | -$1
-2.65 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C7 + D7/2 + F7 + RC_B) * FV | (0 + 5678/2 + 20917 + 11553) * 1 | $35,309 | $35,308 | -$1
-2.6 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C8 + D8/2 + F8 + RC_B) * FV | (1577 + 5678/2 + 20917 + 11553) * 1 | $36,886 | $36,885 | -$1
-2.55 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C9 + D9/2 + F9 + RC_B) * FV | (5624 + 5781/2 + 20917 + 11553) * 1 | $40,985 | $40,984 | -$1
-2.4 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C10 + D10/2 + F10 + RC_B) * FV | (5624 + 5962/2 + 20917 + 11553) * 1 | $41,075 | $41,074 | -$1
-2.24 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C11 + D11/2 + F11 + RC_B) * FV | (5624 + 18020/2 + 23997 + 11553) * 1 | $50,184 | $50,183 | -$1
-2.09 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C12 + D12/2 + F12 + RC_B) * FV | (5624 + 18124/2 + 25575 + 11553) * 1 | $51,814 | $51,813 | -$1
-1.94 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C13 + D13/2 + F13 + RC_B) * FV | (5624 + 19148/2 + 27590 + 11553) * 1 | $54,341 | $54,340 | -$1
-1.79 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C14 + D14/2 + F14 + RC_B) * FV | (7645 + 21882/2 + 37096 + 11553) * 1 | $67,235 | $67,234 | -$1
-1.68 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C15 + D15/2 + F15 + RC_B) * FV | (7645 + 29027/2 + 37096 + 11553) * 1 | $70,808 | $70,807 | $0
-1.48 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C16 + D6/2 + F16 + RC_B) * FV | (7645 + 29582/2 + 37149 + 11553) * 1 | $71,138 | $71,138 | $0
-1.18 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C17 + D17/2 + F17 + RC_B) * FV | (7645 + 29814/2 + 38808 + 11553) * 1 | $72,913 | $72,913 | $0
-0.87 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C18 + D18/2 + F18 + RC_B) * FV | (15148 + 29814/2 + 38808 + 11553) * 1 | $80,416 | $80,415 | -$1
0 | ( Gmech + GS/2 + GB + RC_B ) * FV | (C19 + D19/2 + F19 + RC_B) * FV | (15148 + 29814/2 + 38808 + 11553) * 1 | $80,416 | $80,415 | -$1

## Slide 33: Calc 2: Main Floor
Depth | Equation: | Example: | Values | Calculated: | WHAT IT SHOULD BE | Difference?
0** | ( Gmech + GS/2 + GB + RC_B ) * FV | (C19 + D19/2 + F19 + RC_B) * FV | (15148 + 29814/2 + 38808 + 11553) * 1 | $80,416 | $80,415 | -$1
0.03 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B6 + D6/2 + RC_M)* FV + E19 | (14866 + 3523/2 + 15247) * 1 + 80415 | $112,290 | $112,290 | $1
0.05 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B7 + D7/2 + RC_M)* FV + E19 | (26497 + 5678/2 + 15247) * 1 + 80415 | $124,998 | $124,998 | $0
0.1 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B8 + D8/2 + RC_M)* FV + E19 | (28347 + 5678/2 + 15247) * 1 + 80415 | $126,848 | $126,848 | $0
0.15 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B9 + D9/2 + RC_M)* FV + E19 | (31733 + 5781/2 + 15247) * 1 + 80415 | $130,286 | $130,286 | $1
0.3 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B10 + D10/2 + RC_M)* FV + E19 | (31733 + 5962/2 + 15247) * 1 + 80415 | $130,376 | $130,377 | $1
0.46 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B11 + D11/2 + RC_M)* FV + E19 | (35760 + 18020/2 + 15247) * 1 + 80415 | $140,432 | $140,433 | $1
0.61 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B12 + D12/2 + RC_M)* FV + E19 | (36339 + 18124/2 + 15247) * 1 + 80415 | $141,063 | $141,063 | $0
0.76 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B13 + D13/2 + RC_M)* FV + E19 | (38763 + 19148/2 + 15247) * 1 + 80415 | $143,999 | $144,000 | $1
0.91 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B14 + D14/2 + RC_M)* FV + E19 | (49217 + 21882/2 + 15247) * 1 + 80415 | $155,820 | $155,821 | $1
1.02 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B15 + D15/2 + RC_M)* FV + E19 | (53342 + 29027/2 + 15247) * 1 + 80415 | $163,518 | $163,519 | $1
1.22 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B16 + D16/2 + RC_M)* FV + E19 | (53646 + 29582/2 + 15247) * 1 + 80415 | $164,099 | $164,099 | $0
1.52 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B17 + D17/2 + RC_M)* FV + E19 | (55784 + 29814/2 + 15247) * 1 + 80415 | $166,353 | $166,353 | $0
1.83 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B18 + D18/2 + RC_M)* FV + E19 | (55784 + 29814/2 + 15247) * 1 + 80415 | $166,353 | $166,353 | $0
2.7 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B19 + D19/2 + RC_M + RC_U)* FV + E19 | (55784 + 29814/2 + 15247) * 1 + 80415 | $166,353 | $166,353 | $0

## Slide 34: Calc 3:Upper Floor
Depth | Equation: | Example: | Values | Calculated: | WHAT IT SHOULD BE | Difference?
2.7 | ((GM + GS/2 + RC_M) * FV) + 0** | ( B19 + D19/2 + RC_M + RC_U)* FV + E19 | (55784 + 29814/2 + 15247) * 1 + 80415 | $166,353 | $166,353 | $0

## Slide 35: Response costs
First: Floor Area: * dynamic
  ** X = SUM of all rooms on Main Level
  MFA = Main: X
  BFA = Main: X * % developed basement
  UFA Upper: X
  RC_M = Main: sum(Group_5 General Response cost) * MFA
  RC_B = Basement:
    If BFA != 0 : sum(Group_5 General Response cost) * BFA
    If BFA == RC_U = Upper0: sum(Group_5 Undeveloped Response cost) * undeveloped Area
  RC_U = : sum(Group_5 General Response cost) * UFA
Still working out BFA == 0 Group_5 Response cost
Could set, for now:
sum Group_5 Response cost = 35

## Slide 36: DDF: Area = $/m2
*compute $/Structure DDF first then:
$/structure curve / main floor area (m2)
Round to nearest dollar